## Slide 1: Custom Library
Brandon Moe

## Slide 2: Todays Topics
The Teams Custom VI
How they can be beneficial

## Slide 3: Custom VI and what they mean to you

## Slide 4: Custom VI
A custom VI is one that we have modified to fit our needs
They save us time and accomplish task specific to our team.
These get built upon every year
All of these will be available under the folder 3026 VI

## Slide 5: VI’s explained

## Slide 6: Robot Drive

## Slide 7: Drive Mode
Used to tell the robot what drive mode it is in
Requirements
  none
Returns
  Drive Mode Selected

## Slide 8: MecaTrak
Used in 2016
For the drive train with tank tracks and mecanum wheels

## Slide 9: Open 4 Motors
Used to open a 4 motor Talon SRX CAN drive
Requirements
  4 CAN numbers
  4 motors inverted Boolean
  Control Type
Returns
  Initialized Drive

## Slide 10: Secondary Drive
Used if we have a 6 CIM drive (Which we usually do)
Give the front 2 motor bogus CAN numbers
Requirements
  2 CAN numbers
  2 motors inverted Boolean
  Control Type
Returns
  Initialized Drive

## Slide 11: Turn to angle
Takes in an angle and will turn the robot to that angle
Requirements
  Angle desired (null is -1)
  Z axis
Returns
  Proper rotation value

## Slide 12: Robot Centric
Custom Robot Centric Drive

## Slide 13: Field Centric
Our Custom Field Centric Drive

## Slide 14: Track Button Adjust
Adjust the robot by only turning one motor
Requirements
  Adjust speed
  Buttons for adjustment
  Drive reference num
Returns
  Motors adjusting independently

## Slide 15: “Homie Drive
Used in robot to not flip field orientation from robot centric

## Slide 16: Strafe Correction
On mecanum robots if it is not strafing properly this vi will fix it

## Slide 17: Auto Tracks Down
This will put the tracks down automatically
Requirements
  4 motor values
Returns
  Boolean if tracks should be down

## Slide 18: NavX

## Slide 19: Zero Yaw
This is hooked up to the button on the joystick that will zero the yaw on the NavX
Requirements
  Button
Returns
  None

## Slide 20: Gyro Setup
This will set up the yaw angle so we can use it correctly
Requirements
  Yaw
Returns
  Corrected Yaw

## Slide 21: NavX Variable Get
This will get all of the variables from the NavX
  About 15 variables total

## Slide 22: Vision

## Slide 23: WARNING
Do not touch these only use them!
These are very complex VI that you need years of experience to modify
And trust me these will just give you headaches. Just use them and be grateful.

## Slide 24: RoboRealm
Sets Up Camera
Gives you everything you need to vision track

## Slide 25: Robot Targeting Adjustment
This one you can touch
This is used to adjust the robot for vision targets
When looking at this please parden the mess

## Slide 26: Extras

## Slide 27: Toggle
Used for toggling buttons
LabVIEW did not have one of these VI so we made one
Requirements
  Button input (up to 2)
Returns
  Inputs on toggle

## Slide 28: Joystick Deadband
Used to put a dead band on the joysticks
Requirements
  X, Y, and Z axis
  XY dead band and Z dead band
Returns
  Joystick values with deadband

## Slide 29: Arduino Light Mode
Used for communicating with Arduino
Requirements
  The 4 Boolean values
Returns
  Arduino with correct lights

## Slide 30: Proximity Display
It is essentially this
Requirements
  4 ultrasonic sensors

## Slide 31: Lab 3
Place the toggle VI in teleop x2
Place the Joystick deadband in teleop x2
Place the Zero Yaw in teleop
Place the Arduino Light Mode in teleop