## Slide 1: Lecture 3
Brandon Moe

## Slide 2: Todays Lesson
The RoboRio
The Radio
Parts of a robot
What they mean to you

## Slide 3: RoboRio

## Slide 4: What is it?
The computer on the robot
Processes your code and executes it.
Fun fact: runs on NI Linux Operating System

## Slide 5: Facts about the RoboRio
2 CPU
IP Address: 172.22.11.2
If connected to robot you can use 10.30.26.2
Connect through router, Ethernet to Rio, or USB B
Runs on 24 Volts

## Slide 6: RoboRio Web Interface

## Slide 7: Walk through of interface

## Slide 8: IP Addresses to Know
Your PC: 10.30.26.5
UP Board 1: 10.30.26.11
UP Board 2: 10.30.26.12
RoboRio: 10.30.26.2
  172.22.11.2 if not connected to wifi with code

## Slide 9: Steps for brand new Rio
Image the Rio using the FRC imaging tool
  Set Team Number to 3026
Set the IP Address to static on web interface
  IP address: 10.30.26.2
  Subnet Mask: 255.0.0.0
  Gateway: 10.30.26.1
Check for any errors
Update Radio Using CTRE HERO imaging tool

## Slide 10: RoboRio Imaging Tool

## Slide 11: CTRE HERO Imaging Tool

## Slide 12: Radio

## Slide 13: Facts about Radio
2 Ethernet slots
Runs on 12 V 1 Amp
Speed: 1.17 Gbps (300+867 Mbps)
Radio: 802.11b/g/n 2.4 GHz + 802.11a/n/ac 5 GHz
Antenna: Two internal dual band 2x2 (2.4 GHz) + 2x2 (5 GHz)
Range (approximate): 25-50’ indoor (1-2 walls) 100’ outdoor
Processor: 720 MHz QCA9557 + QCA9882 MIPS 74K
It sucks at connecting

## Slide 14: How to format a radio
FRC Radio Configuration Utility

## Slide 15: Different Parts of a robot

## Slide 16: Drive Train
This moves the robot around
6 CIMS
6 Talon SRX
Will be a combination of Tank drive and mecanum wheels
NavX will be used

## Slide 17: Manipulator
Moves around game pieces
Includes and not limited to
  Servos
  Talon SRX
  Variety of motors

## Slide 18: Pneumatics
This is all of the air on the robot
  Controlled by the PCM (Pneumatic Control Module)
Includes
  Solenoids
  PCM
  Compressor
  Transducer
We will be using pneumatics on all robots

## Slide 19: What does this mean to me

## Slide 20: You Need to know the hardware
You CAN NOT program a robot without knowing what you are programming
However you do not need to be a hardware expert
  that's why we have a hardware team
Know all of the functions of all robot parts and there limitation

## Slide 21: Examples
Amp limit on CIMS are 70 amps
DO NOT STALL 775 pros
The Talon SRX can do anything you want to
  Trust me I've tried to find its limitation, it doesn’t exist
CIMS have a duty cycle of 5-7 minutes
Make sure solenoids are not fighting each other

## Slide 22: Always set fail safes
You are the last defense between our robot and the driver
Ex:
  2016 Arm can not go below ground level or above 90 degrees
  2017 Robot when it climbs it goes into safe mode
    Joystick 2 is disabled
    All manipulator come inside of robot
    Climber has an amp limit

## Slide 23: Build and programming team vs Driver
When competition arrives drivers are told to drive it like you stole it
They will drive it to the breaking point and do anything to preform at their best
Make your program so they can get to that point but limits the robot before it breaks

## Slide 24: Example of failsafe
Fails test
Passes test

## Slide 25: Lab 2
Write a VI with the following
  Take a number off of a slider
  Your code should accept values from 2-7
  It should default to 5 if error occures
  Any other number shoud be thrown out
  Output should go to a numeric indicator
  This code should run continusly
    Hint: while loop

## Slide 26: Turn In procedure
Upload VI into Extra VI’s folder
  Name Lab 2